## Slide 1: Introduction to Optimization in Generic Algebraic Modeling System (GAMS)
26th June 2022
Presented by:
Dr. Muhammad Nurariffudin
Universiti Teknologi Malaysia (UTM)

## Slide 2: Objectives of this workshop
To understand the concept of optimisation and its associated components
2) To formulate mathematical optimization problems based on manual and software approaches
3) To code the optimization model into an optimisation software, Generalised Algebraic Modeling System (GAMS)
4) To perform scenario analysis for the evaluation of variable renewable energy (vRE) and analyse the impact on microgrid power generation scheduling

## Slide 3
Expected Outcomes
By the end of the course, the participant should be exposed to:
Fundamental concept of optimisation
Applications of optimization in various fields
Terminology in process optimization - objective function, decision variables and constraints
Formulating an Optimisation Model

## Slide 4: Why Optimisation
What can happen with poor or no appropriate optimisation models?
Very Costly Lessons!

## Slide 5: Application of Optimization Models
Example: A Utility Company
Fuel
Heat Energy
(Steam)
GHG
Utility Plant
Chemical Plant
But remember, there
are always trade-offs (good/bad)
to be considered

## Slide 6: Application of Models
Example: A Utility Company
Plant Size (ton/hr)
Cost
($/ton)
Fuel Cost +
Carbon Emission Cost
Utility Plant Cost
Optimum

## Slide 7
Why Optimization?
economic incentives:
  maximise profit
  minimise costs
  maximise use of resources
  minimise effort
technical incentives:
  safer design and operating strategy
  Better processing strategy
  increased yield, conversion
  optimum selectivity
  minimum holdup
integral part of design and operation:
  optimisation of process structure (synthesis)
  optimisation of operation
  technical/economic
  control
environmental incentives:
  Minimise carbon emission
  Minimise environmental impact

## Slide 8
Definition of Optimisation
Finding the best solution to achieve the goal subject to a set of constraint
The purpose of optimization is to maximize (or minimize) the value of a function (called objective function) subject to a number of restrictions (called constraints).

## Slide 9: Key elements of Optimisation
Objective function
  mathematical function to be minimised or maximised, related to the desired incentives by the company
Decision variables
  variables that you can adjust or choose in order to minimize or maximize the objective function
  variables can be:
    Continuous, e.g. flowrates, concentration, temperature, pressure
    Integers, eg. # of trays
    Binary (either 0 or 1), eg. Select/not select - plant process flowsheet

## Slide 10
Key elements of Optimisation
Parameters
  variables that predefined by the users.
  eg. Cost of the product
Constraints
  Limitations or restrictions of decision variables.
  can be physical, economic, policy, or environmental constraints
  can be either equality constraints or inequality constraints

## Slide 11: Equality Constraints
Equality constraints, hk (x) = 0,
represent process restrictions:
  Product purity must be exactly 98%
represent the process model:
    The heat and material balance
    Mole fraction summation equations
    Equilibrium equations, etc.

## Slide 12: Inequality Constraints
Inequality constraints, gj (x) ≥ 0,
represent restrictions imposed by the designer and by nature.
Mole fraction flowrate must be greater than or equal to zero (no negative flowrates are allowed)
Pressure in a particular vessel cannot exceed an upper limit
A reactor volume cannot exceed the maximum currently manufactured
Production rates and product purities must all be greater than minimum values.

## Slide 13: Classification of optimisation problem

## Slide 14: Classification of optimisation problem

## Slide 15: Classification of optimisation problem

## Slide 16: Classification of optimisation problem

## Slide 17: Example 1: Nutrient Requirements

## Slide 18: Solution to Example 1

## Slide 19: Example 2: Production of Tongkat Abu

## Slide 20: Solution to Example 2

## Slide 21: Working Session: Solar Photovoltaic
Ahmad plan to install solar power generation in his house. By looking at the profile of hourly solar radiation and house electricity demand, identify
1. Objective Function
2. Decision variables
3. Parameter
4. Constraints
Chart: Solar Irradiation
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.028212 | 0.16645 | 0.34343 | 0.51119 | 0.63695 | 0.71436 | 0.72238 | 0.66179 | 0.54852 | 0.39157 | 0.21876 | 0.069345 | 0.0015069 | 0 | 0 | 0 | 0
Chart: Electricity Demand (kWh)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Residential | 67.3928 | 63.5138 | 59.9023 | 56.8258 | 55.3544 | 55.0869 | 56.0232 | 48.1314 | 49.8703 | 56.2907 | 61.2399 | 62.9788 | 60.5711 | 59.6348 | 63.1125 | 63.9151 | 63.5138 | 59.7685 | 58.0296 | 67.2591 | 73.4121 | 73.0108 | 69.9343 | 66.724

## Slide 22
Generalized Algebraic Modeling Systems
GAMS is a high-level modeling system for mathematical programming
GAMS is a programming language that comes with
- a language compiler, and
- an integrated solver.
GAMS allows for the construction
and solution of large and complex
algebraic models
Generalized Algebraic
Modeling System

## Slide 23
A programming
language compiler
An integrated solver
GAMS system
Generalized Algebraic Modeling System

## Slide 24: Generic Algebraic Modeling System (GAMS)
GAMS is a high level modeling system for mathematical programming and optimization.
The GAMS modeling language allows modelers to quickly translate real world optimization problems into computer code.
The handling of different mathematical optimization problems (e.g., LP, MILP, NLP, MINLP, stochastic) is done through a variety of mathematical solvers (e.g., CPLEX, GUROBI, CBC, BARON) that translate the formulations into results.
The latest GAMS version offers two software platforms, namely GAMS Studio and GAMS IDE.
GAMS IDE is traditional platform used since the early days of GAMS application. GAMS Studio is a more user friendly platform as an alternative to GAMS IDE. In GAMS Studio, advanced functionality can be accessed, namely GAMS MIRO for web-based user interface and GAMS Engine for running large-scale models and scenarios.
GAMS IDE
GAMS Studio

## Slide 25
SETS
VARIABLES
PARAMETERS
EQUATION
MODEL
SOLVE
General GAMS Structure
GAMS inputs

## Slide 26
SETS
- Declaration
- Assignment of members
DATA (PARAMETERS, SCALARS, TABLES)
- Declaration
- Assignment of values
VARIABLES
- Declaration
- Assignment of types
- Assignment of bounds (optional)
- Assignment of initial values (optional)
General GAMS Structure
GAMS Inputs

## Slide 27: Important Syntax Features of GAMS
Sets
Indices related to the algebraic representation of the model. Often used to categorize data and variables that have similar representation.
Example :
    Hours in a day - 1am, 2am, 3am, 4am, 5am, 6am, 7am, 8am, 9am, 10am, 11am, 12am, 1pm, ………..
    Types of fuels - Coal, oil, gas, biomass, solar, wind
Example syntax:

## Slide 28
Parameters
Parameters are the data that needs to be inputted in GAMS in order for the model to work
Example:
  Electricity tariffs, hourly solar irradiation, hourly energy demand, technology efficiency, investment cost, operating cost
Example syntax
Important Syntax Features of GAMS

## Slide 29: Important Syntax Features of GAMS
Variables
Variables are the “unknown” quantity in an optimization problem or the “outputs” that needs to calculated from the mathematical problem. There are several types of variables declaration in GAMS, such as free variable (usually the objective function), positive variable, binary variable, and integer variable. The default in GAMS is free variable.
Example
    Free variable: Total system cost, total system emission
    Positive variable: Electricity production rate, charging/discharging rate, fuel supply
    Binary variable: Allowance to charge at certain hour, allowance to chose one technology from sets of technology
    Integer variable: Number of PV units, number of turbine units, number of power plants
Example syntax

## Slide 30: Important Syntax Features of GAMS
Equation list:
Representing the declaration of equation name.
  Example syntax:
Equations: Equations that needs to be formulated to form an optimization model. Note: =E= reflects equal symbol, =L= reflects less than or equal symbol, =G= reflects greater than or equal symbol.
  Example syntax:
Double dot or .. is a must after an equation name
To write comment, start with asterisk * (optional)
End each equation with semicolon ;

## Slide 31: Important Syntax Features of GAMS
Model Statement: This syntax is used to name your optimization model and select the equations to be included in the modeling runs. Commonly, ALL equations are included to run the optimization model.
  Example syntax:
Solve Statement: The solve statement (1) tells GAMS which model to solve, (2) selects the solver to use (in this case an LP solver), (3) indicates the direction of the optimization, either MINIMIZING or MAXIMIZING , and (4) specifies the objective variable.
  Example syntax:

## Slide 32: Important Files for Common GAMS Problem
ModelName.gms
- The file to be run containing all of the mathematical formulation syntax
ModelName.lst
- File containing the details of the modeling outputs
Process Log or ModelName.log
- Highlight the status of the model runs, objective function, errors, and key model settings.

## Slide 33: GDX File for Convenient Viewing of Modeling Outputs (Optional)
Additional syntax needs to be added in the model after the solve statement to compile all outputs in GDX file (a file compiling all the outputs in a tabular form).
    Example syntax:

## Slide 34: Steps to Install GAMS
Step 1: Please go the https://www.gams.com/try_gams/ and fill in your information to request a demo license. Please note that the demo license has limited functionality (It can handle a maximum of 2000 variables and 2000 constraints).
Step 2: Go to https://www.gams.com/download/, and download the latest version of GAMS software.
Step 3: Install GAMS. At the end of the installation process, there will be an instruction to upload the license file. If you miss the step to upload the license file, copy the information in the license file to your clipboard, open GAMS Studio, click Help>GAMS Licensing, and click yes on the instruction to upload the license file.
Step 4: Explore the GAMS software and run your models.

## Slide 35
FORMULATION OF OPTIMISATION MODEL

## Slide 36: GENERAL PROCEDURE TO FORMULATE AN OPTIMIZATION PROBLEM
STEP 1. DEFINE THE DECISION VARIABLES
STEP 2. DEFINE THE OBJECTIVE FUNCTION
STEP 3. DEVELOP PROCESS OR EQUIPMENT
MODEL USING PHYSICAL/EMPIRICAL
CORRELATION
- INCLUDE EQUALITY & INEQUALITY
CONSTRAINTS
STEP 4. APPLY SUITABLE SOLUTION TECHNIQUE
e.g graphical method vs optimization tools
STEP 5. PERFORM SENSITIVITY ANALYSIS
PROBLEM
FORMULATION
PROBLEM
SOLVING

## Slide 37
STEPS
SET definitions (refineries, markets)
2. Data entry
(cost, supply, demand)
3. Variable specifications
4. Equation declaration
5. Equation specification
5. Model statement
6. Solve statement
7. Display statement

## Slide 38: Fertilizer Example

## Slide 39: Formulation

## Slide 40: GAMS

## Slide 41: RESULT

## Slide 42: Two Crude Petroleum

## Slide 43: Two Crude Petroleum

## Slide 44: Formulation

## Slide 45: GAMS

## Slide 46: RESULT

## Slide 47: Introduction to Superstructure
Rule of thumb:
Availability ≥ Supply (Bounded)
Or
Availability ≥ Supply (Not Bounded)
Supply ≤ Demand (Bounded)
Or
Supply ≤ Demand (Bounded)

## Slide 48: Introduction to Superstructure

## Slide 49: Introduction to Superstructure

## Slide 50: Introduction to Superstructure

## Slide 51: Introduction to Superstructure

## Slide 52: Introduction to Superstructure

## Slide 53: Power Distribution

## Slide 54: Power Distribution

## Slide 55: Formulation

## Slide 56: Formulation

## Slide 57: GAMS

## Slide 58: RESULT

## Slide 59
OPTIMIZATION APPLICATION – SOLVING SCHEDULING PROBLEM

## Slide 60: Importance of scheduling
Schedules are plans that state when certain controllable activities should take place
Schedules provide a coordination of activities to:
  Increase productivity
  Reduce operating costs
  Identify resource conflicts
  Ensure raw material is available
  Standardize the production process etc.

## Slide 61: Importance of scheduling
Schedule is generated
Operations begin
Schedule is followed as closely as possible
Achievement of program objectives

## Slide 62: Roles of Scheduling in Planning Process
Short-term planning
Medium-term planning
Long-term planning

## Slide 63: Roles of Scheduling in Planning Process
Short-term planning
Medium-term planning
Long-term planning
Covers a period of more than 1 year
E.g., 3-5 years
Objective: Set plan for future activities; set investment schedules
Covers a period of within one year
E.g., month, seasons
Objective: Set maintenance schedule; shutdown
Covers a period of 1 day to 1 week
E.g., minutes, hours, days
Objective: Hourly operations; Day-to-day scheduling

## Slide 64: Roles of Scheduling in Planning Process
Short-term planning
Medium-term planning
Long-term planning
Covers a period of more than 1 year
E.g., 3-5 years
Objective: Set plan for future activities; set investment schedules
Covers a period of within one year
E.g., month, seasons
Objective: Set maintenance schedule; shutdown
Covers a period of 1 day to 1 week
E.g., minutes, hours, days
Objective: Hourly operations; Day-to-day scheduling

## Slide 65: Scheduling Aspect in Electricity System: Daily electricity consumption by electrical appliances
Source: Le, V. T., & Pitts, A. (2019). A survey on electrical appliance use and energy consumption in Vietnamese households: Case study of Tuy Hoa city. Energy and Buildings, 197, 229-241.
Source: McNeil, M. A., Karali, N., & Letschert, V. (2019). Forecasting Indonesia's electricity load through 2030 and peak demand reductions from appliance and lighting efficiency. Energy for sustainable development, 49, 65-77.
Electricity Consumption by Electrical Appliances
Hourly Load Profiles of Electricity Consumption

## Slide 66: Scheduling Aspect in Electricity System: Different types of electricity load profiles
Source: Jain, A., Mani, A., & Siddiqui, A. S. (2019). Network architecture for demand response implementation in smart grid. International Journal of System Assurance Engineering and Management, 10(6), 1389-1402.

## Slide 67: Scheduling Aspect in Electricity System: Power system operation
Generation must equal load plus transmission losses (about 5%)

## Slide 68: Scheduling Aspect in Electricity System: Power system operation
What happens if a generator fails?
  When load is greater than generation the system slows down
  If nothing is done the system shuts down completely

## Slide 69: Scheduling Aspect in Electricity System: Solar PV Addition in Electrical Load

## Slide 70
Source: Marcucci, A., & Turton, H. (2012). Swiss energy strategies under global climate change and nuclear policy uncertainty. Swiss journal of economics and statistics, 148(2), 317-345.
Source: Zappa, W., Junginger, M., & Van Den Broek, M. (2019). Is a 100% renewable European power system feasible by 2050?. Applied energy, 233, 1027-1050.

## Slide 71
A power system operator receives an information that total coal and natural gas based electricity that are available for the next day operation are at 500 MWh and 2000 MWh per day, respectively, which cost at 40 USD/MWh and 50 USD/MWh. Given the electricity demand needed to be fulfilled at each hour, you are required to generate optimal scheduling operation for the power system operator at the lowest cost.
Exercise 1: Power system operation
Hour | Demand (MWh)
1 | 30
2 | 30
3 | 29
4 | 29
5 | 31
6 | 30
7 | 30
8 | 32
9 | 34
10 | 35
11 | 35
12 | 34
13 | 35
14 | 36
15 | 36
16 | 35
17 | 35
18 | 36
19 | 38
20 | 37
21 | 37
22 | 36
23 | 34
24 | 33

## Slide 72
Step 1: Define decision variables
  x1(t) – coal-based electricity generation (MWh)
  x2(t) – natural gas-based electricity generation (MWh)
Step 2: Define the objective function
  Minimize cost = 40 * sum(t,x1(t)) + 50 * sum(t,x2(t))
Step 3: Define the equality and inequality constraints
  Coal-based electricity availability:
  sum(t,x1(t)) =l= a1;
  Natural gas-based electricity availability:
  sum(t,x2(t)) =l= a2;
  Electricity demand
  x1(t) + x2(t) =e= d1(t);
Exercise 1: Power system operation

## Slide 73
Exercise 1: GAMS Formulation

## Slide 74
Exercise 1: GAMS Results
Chart: Load Profile
Coal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 21 | 35 | 36 | 38 | 37 | 37 | 36 | 34 | 33
Natural Gas | 30 | 30 | 29 | 29 | 31 | 30 | 30 | 32 | 34 | 35 | 35 | 34 | 35 | 36 | 36 | 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Natural Gas

## Slide 75
A power system operator receives an information that total coal, natural gas, oil, nuclear, and hydropower based electricity that are available for the next day operation are at 200 MWh, 200 MWh, 100 MWh, 1000 MWh, and 100 MWh respectively, which cost at 40 USD/MWh, 50 USD/MWh, 35 USD/MWh, 60 USD/MWh, and 30 USD/MWh. Given the electricity demand needed to be fulfilled at each hour, you are required to generate optimal scheduling operation for the power system operator at the lowest cost.
Exercise 2: Power system operation
Hour | Demand (MWh)
1 | 30
2 | 30
3 | 29
4 | 29
5 | 31
6 | 30
7 | 30
8 | 32
9 | 34
10 | 35
11 | 35
12 | 34
13 | 35
14 | 36
15 | 36
16 | 35
17 | 35
18 | 36
19 | 38
20 | 37
21 | 37
22 | 36
23 | 34
24 | 33

## Slide 76
Exercise 2: GAMS Formulation

## Slide 77
Exercise 2: GAMS Results
Chart: Load Profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Coal | 29 | 29 | 34 | 37 | 37 | 34
Natural Gas | 35 | 21 | 36 | 36 | 36 | 36
Oil | 30 | 10 | 30 | 30
Nuclear | 20 | 31 | 3 | 35 | 34 | 14 | 35 | 35
Hydropower | 29 | 38 | 33

## Slide 78
A power system operator receives an information that total coal, natural gas, oil, nuclear, and hydropower based electricity that are available for the next day operation are at 100 MWh, 100 MWh, 100 MWh, 500 MWh, and 200 MWh respectively, which cost at 40 USD/MWh, 50 USD/MWh, 35 USD/MWh, 60 USD/MWh, and 30 USD/MWh. The operator wants to also integrate renewable energy in their operation based on solar which costs at 42 USD/MWh. Given the solar availability and electricity demand needed to be fulfilled at each hour, you are required to generate optimal scheduling operation for the power system operator at the lowest cost.
Exercise 3: Power system operation
Hour | Demand (MWh) | Solar Electricity Availability (MWh)
1 | 30 | 0
2 | 30 | 0
3 | 29 | 0
4 | 29 | 0
5 | 31 | 0
6 | 30 | 0
7 | 30 | 2.4
8 | 32 | 8.4
9 | 34 | 15
10 | 35 | 20.8
11 | 35 | 24.9
12 | 34 | 26.9
13 | 35 | 26.6
14 | 36 | 23.9
15 | 36 | 19.2
16 | 35 | 13
17 | 35 | 6.5
18 | 36 | 1.3
19 | 38 | 0
20 | 37 | 0
21 | 37 | 0
22 | 36 | 0
23 | 34 | 0
24 | 33 | 0

## Slide 79
Exercise 3: GAMS Formulation

## Slide 80
Exercise 3: GAMS Results
Chart: Load Profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Coal | 5.1 | 14.2 | 10.1 | 7.1 | 8.4 | 12.1 | 16.8 | 22 | 4.2
Natural Gas | 23.6 | 13.9 | 37 | 25.5
Oil | 29 | 0.9 | 31 | 27.6 | 11.5
Nuclear | 30 | 30 | 28.1 | 30
Hydropower | 24.3 | 34.7 | 38 | 36 | 34 | 33
Solar | 0 | 0 | 0 | 0 | 0 | 0 | 2.4 | 8.4 | 15 | 20.8 | 24.9 | 26.9 | 26.6 | 23.9 | 19.2 | 13 | 6.5 | 1.3 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 81: More concrete examples on scheduling
We will learn how to code the mathematical problem in GAMS and solve it to generate results.
Electricity scheduling problems are chosen as the cases to be studied in these exercises.
Three cases will be considered, namely Solar PV Integration, Solar PV Integration with Battery Storage, and Off-grid Solar PV Integration.
The objectives of evaluating the two cases include:
  Evaluating the load profile pattern after the solar PV integration.
  Identifying the costs of solar PV integration with and without battery storage contribution.
  Identifying the scales of solar PV microgrid needed for the two cases.

## Slide 82: Electricity Scheduling Problems: Solar PV Integration
Problem:
A group of residential customers are planning to install the Solar PVs in their houses. Previously, subscription of grid electricity to power their homes cost them a total of about USD 29,281.76/year of electricity bills. The customers want to know what are the maximum capacities of Solar PV that can be installed in their areas to save their electricity bills. Given this problem, you are requested to build a model to calculate optimal solar PV integration rate for cost savings of their houses based on a given parameter of a hourly electricity demand. Provided below are the related parameters that can be used for your calculation.
Parameters | Parameters
Solar PV CAPEX: 1500 USD/kW | Solar PV lifetime: 20 years
Solar PV OPEX: 15 USD/kW/year | Inverter lifetime: 10 years
Inverter CAPEX: 60 USD/kW | Solar PV efficiency: 0.18
Electricity tariff: 0.0545 USD/kWh | Inverter efficiency: 0.96
Interest rate: 3% | Solar PV power density: 0.08 kW/m2
Input Data

## Slide 83: Electricity Scheduling Problems: Solar PV Integration
Chart: Solar Irradiation
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.028212 | 0.16645 | 0.34343 | 0.51119 | 0.63695 | 0.71436 | 0.72238 | 0.66179 | 0.54852 | 0.39157 | 0.21876 | 0.069345 | 0.0015069 | 0 | 0 | 0 | 0
Hour | Solar Irradiation (kW/m2) | Electricity Demand (kWh)
0 | 0 | 67
1 | 0 | 64
2 | 0 | 60
3 | 0 | 57
4 | 0 | 55
5 | 0 | 55
6 | 0 | 56
7 | 0.02821 | 48
8 | 0.16645 | 50
9 | 0.34343 | 56
10 | 0.51119 | 61
11 | 0.63695 | 63
12 | 0.71436 | 61
13 | 0.72238 | 60
14 | 0.66178 | 63
15 | 0.54851 | 64
16 | 0.39157 | 64
17 | 0.21876 | 60
18 | 0.06934 | 58
19 | 0.0015 | 67
20 | 0 | 73
21 | 0 | 73
22 | 0 | 70
23 | 0 | 67
Chart: Electricity Demand (kWh)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Residential | 67.3928 | 63.5138 | 59.9023 | 56.8258 | 55.3544 | 55.0869 | 56.0232 | 48.1314 | 49.8703 | 56.2907 | 61.2399 | 62.9788 | 60.5711 | 59.6348 | 63.1125 | 63.9151 | 63.5138 | 59.7685 | 58.0296 | 67.2591 | 73.4121 | 73.0108 | 69.9343 | 66.724
Input Data

## Slide 84: Electricity Scheduling Problems: Solar PV Integration
Step 1: Define SET
  T = set of hours in a day
Step 2: Define available PARAMETERS
  SolarIrradianceT = Solar Irradiation at hour T (kW/m2)
  ElectricityDemandT = Electricity demand at hour T (kWh)
  SolarEfficiency = Efficiency of solar PV
  InverterEfficiency = Efficiency of inverter to convert DC electricity from solar to AC
  SolarAreaDensity = Solar PV power density (kW/m2)
  ElectricityTariff = Electricity tariff (USD/kWh)
  SolarInvestmentCost = Investment cost of solar PV (USD/kW)
  SolarOperatingCost = Investment cost of solar PV (USD/kW/year)
  InverterInvestmentCost = Investment cost of inverter (USD/kW)
  i = Interest rate
  SL = Solar PV lifetime (year)
  IL = Inverter lifetime (year)
Step 3: Define DECISION VARIABLES
  SolarEnergyProducedT = Electricity generation from solar PV at hour T (kWh)
  EnergyFromGridT = Electricity from the grid at hour T (kWh)
  As solar irradiance parameter listed above is in kW/m2, we need to convert it into kWh unit to ensure similar unit is being used for the energy balance. Thus, MicrogridAreaSolar in m2 = Area needed for solar PV installation, is declared as a variable to cancel out the unit.
  InverterCapacitySolar = Capacity of inverter (kW)
Steps to Develop a Mathematical Model

## Slide 85: Electricity Scheduling Problems: Solar PV Integration
Step 4: Define OBJECTIVE FUNCTION
  Minimize TotalCost of meeting electricity demand from solar PV and grid.
  TotalCost = MicrogridAreaSolar x SolarAreaDensity x [SolarInvestmentCost * AnnualizedInvestmentFactorSolar + Operating Cost]
  + InverterCapacity x InverterInvestmentCost x AnnualizedInvestmentFactorInverter
  + x ElectricityTariff x 365
Step 5: Define CONSTRAINTS
  Solar Energy Supply: SolarEnergyProducedT = MicrogridAreaSolar x SolarIrradianceT x SolarEfficiency
  Electricity Demand: SolarEnergyProducedT + EnergyFromGridT = ElectricityDemandT
  Inverter Capacity: SolarEnergyProducedT ≤ InverterCapacity
Step 6: CODE the mathematical formulation in GAMS
Annualized Investment Factor =
Where, i is interest rate, lifetime is the economic life of a technology
Note:
Steps to Develop a Mathematical Model

## Slide 86: Electricity Scheduling Problems: Solar PV Integration
Sets and parameters

## Slide 87: Electricity Scheduling Problems: Solar PV Integration
Declarations of variables and equations

## Slide 88: Electricity Scheduling Problems: Solar PV Integration
Mathematical formulations
Model and solve statements

## Slide 89: Electricity Scheduling Problems: Solar PV Integration
Results:
Objective function = 25,890.078161 USD/year
Microgrid area = 480.666 m2
Electricity production: 1,472 kWh/day (28% solar penetration)
Cost savings:
29,281.76 USD/year (Reference) – 25,890.078161 USD/year
= 3,391.68 USD/year
Chart: Hour of the day
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Grid Electricity | 67 | 64 | 60 | 57 | 55 | 55 | 56 | 45.6569 | 36.1749 | 27.4751 | 18.5412 | 10.0957 | 1.6661 | 0 | 8.0334 | 18.4414 | 31.4767 | 41.8301 | 52.2407 | 66.8754 | 73 | 73 | 70 | 67
Solar PV | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.3431 | 13.8252 | 28.5249 | 42.4588 | 52.9043 | 59.3339 | 60 | 54.9666 | 45.5585 | 32.5234 | 18.1699 | 5.7593 | 0.12459 | 0 | 0 | 0 | 0
Hour | Grid Electricity | Solar PV
0 | 67 | 0
1 | 64 | 0
2 | 60 | 0
3 | 57 | 0
4 | 55 | 0
5 | 55 | 0
6 | 56 | 0
7 | 45.6569 | 2.343091
8 | 36.1749 | 13.82515
9 | 27.4751 | 28.52486
10 | 18.5412 | 42.45878
11 | 10.0957 | 52.90426
12 | 1.66613 | 59.33386
13 | 0 | 60
14 | 8.03336 | 54.96662
15 | 18.4414 | 45.55853
16 | 31.4767 | 32.52336
17 | 41.8301 | 18.16992
18 | 52.2407 | 5.759299
19 | 66.8754 | 0.124588
20 | 73 | 0
21 | 73 | 0
22 | 70 | 0
23 | 67 | 0
Please note to multiply SolarEnergyProducedT with inverter efficiency in the results to reflect the converted electricity values.
Load (kWh)

## Slide 90: Electricity Scheduling Problems: Solar PV Integration with Battery
Problem:
Similar case involving the fulfilment of electricity demand in residential areas is considered here. However, the customers are interested in enhancing the solar PV shares to power their homes. For this reason, battery energy storage is needed to store energy to increase the solar PV penetration at night. Based on this problem, you are requested to build a model to calculate optimal solar PV integration with battery contribution based on a given parameter of a hourly electricity demand (assuming 50% VRE penetration target, which is higher than the optimal rate in previous case at 28%, to force the battery contribution).
Note: Use the previous model and extend it for this application.
Parameters | Parameters
Battery-Energy CAPEX: 380 USD/kWh | VRE penetration target: 50%
Battery-Power CAPEX: 360 USD/kW | Battery lifetime: 10 years
Battery-Power OPEX: 10 USD/kW/year | Battery charging efficiency: 0.94
Battery depth-of-discharge: 80% | Battery discharging efficiency: 0.94
Additional Input Data

## Slide 91: Electricity Scheduling Problems: Solar PV Integration with Battery
Sets and parameters

## Slide 92: Electricity Scheduling Problems: Solar PV Integration with Battery
Declaration of variables and equations

## Slide 93: Electricity Scheduling Problems: Solar PV Integration with Battery
Mathematical formulations

## Slide 94: Electricity Scheduling Problems: Solar PV Integration with Battery
Mathematical formulations

## Slide 95: Electricity Scheduling Problems: Solar PV Integration with Battery
Results:
Objective function = 35091.368572 USD/year
Microgrid area = 876.659 m2
Electricity production: 1,472 kWh/day (50% solar penetration)
Cost increment:
35,091.368572 USD/year - 29,281.76 USD/year (Reference)
= 5,809.61 USD/year
Please note to multiply SolarEnergyProducedT with inverter efficiency and SolarEnergyStorageDischargedT with inverter efficiency and discharge efficiency in the results to reflect the converted electricity values.
Hour | Grid Electricity | Solar PV | Battery
0 | 67 | 0 | 0
1 | 64 | 0 | 0
2 | 60 | 0 | 0
3 | 57 | 0 | 0
4 | 55 | 0 | 0
5 | 55 | 0 | 0
6 | 56 | 0 | 0
7 | 43.7266 | 4.27344 | 0
8 | 24.785 | 25.21498 | 0
9 | 3.97491 | 52.02509 | 0
10 | 0 | 61.00003 | 0
11 | 0 | 63 | 0
12 | 0 | 61.00003 | 0
13 | 0 | 60 | 0
14 | 0 | 63 | 0
15 | 0 | 64.00003 | 0
16 | 4.68234 | 59.31763 | 0
17 | 26.8608 | 33.1392 | 0
18 | 47.4959 | 10.50413 | 0
19 | 66.7728 | 0.22723 | 0
20 | 33.0971 | 0 | 39.90286
21 | 26.5349 | 0 | 46.46512
22 | 23.5349 | 0 | 46.46512
23 | 20.5349 | 0 | 46.46512
Load (kWh)
Chart: Hour of the day
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Grid Electricity | 67 | 64 | 60 | 57 | 55 | 55 | 56 | 43.7266 | 24.785 | 3.9749 | 0 | 0 | 0 | 0 | 0 | 0 | 4.6823 | 26.8608 | 47.4959 | 66.7728 | 33.0971 | 26.5349 | 23.5349 | 20.5349
Solar PV | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.2734 | 25.215 | 52.0251 | 61 | 63 | 61 | 60 | 63 | 64 | 59.3176 | 33.1392 | 10.5041 | 0.22723 | 0 | 0 | 0 | 0
Battery | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 39.9029 | 46.4651 | 46.4651 | 46.4651

## Slide 96: Electricity Scheduling Problems: Off-Grid Solar PV Integration
Problem:
For this problem, you are requested to apply the previous model (Solar PV Integration with Battery) to assess off-grid solar PV integration with battery based on a given parameter of a hourly electricity demand (assuming 100% VRE penetration target to resemble the off-grid application).
Note: Use the previous model and extend it for this application.

## Slide 97: Electricity Scheduling Problems: Off-Grid Solar PV Integration
Results:
Objective function = 69,922.459796 USD/year
Microgrid area = 1,826.32 m2
Electricity production: 1,472 kWh/day (100% solar penetration)
Cost increment:
69,922.45979 USD/year - 29,281.76 USD/year (Reference)
= 40,640.70 USD/year
Please note to multiply SolarEnergyProducedT with inverter efficiency and SolarEnergyStorageDischargedT with inverter efficiency and discharge efficiency in the results to reflect the converted electricity values.
Hour | Grid Electricity | Solar PV | Battery
0 | 0 | 0 | 67.00004
1 | 0 | 0 | 64.00001
2 | 0 | 0 | 60.00003
3 | 0 | 0 | 57.00001
4 | 0 | 0 | 55.00002
5 | 0 | 0 | 55.00002
6 | 0 | 0 | 55.99997
7 | 0 | 8.902723 | 39.09729
8 | 0 | 49.99997 | 0
9 | 0 | 55.99997 | 0
10 | 0 | 61.00003 | 0
11 | 0 | 63 | 0
12 | 0 | 61.00003 | 0
13 | 0 | 60 | 0
14 | 0 | 63 | 0
15 | 0 | 64.00003 | 0
16 | 0 | 64.00003 | 0
17 | 0 | 60 | 0
18 | 0 | 21.88282 | 36.11721
19 | 0 | 0.473381 | 66.52664
20 | 0 | 0 | 73.00001
21 | 0 | 0 | 73.00001
22 | 0 | 0 | 69.99998
23 | 0 | 0 | 67.00004
Load (kWh)
Chart: Hour of the day
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Grid Electricity
Solar PV | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8.9027 | 50 | 56 | 61 | 63 | 61 | 60 | 63 | 64 | 64 | 60 | 21.8828 | 0.47338 | 0 | 0 | 0 | 0
Battery | 67 | 64 | 60 | 57 | 55 | 55 | 56 | 39.0973 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 36.1172 | 66.5266 | 73 | 73 | 70 | 67

## Slide 98: Advanced Functionality: Data Exchange with Microsoft Excel
Input
Output
Data Exchange in GAMS using Excel as an interface

## Slide 99: Advanced Functionality: Data Exchange with Microsoft Excel
Using the first case, Solar PV Integration, we can transform the model into using excel as an interface by modifying the declaration of input and output data.
Previous codes
Added codes
Data previously inputted in GAMS needs to be removed

## Slide 100: Advanced Functionality: Data Exchange with Microsoft Excel
Added codes (enlarged)
Put the name of your excel input data.
Put the name of the first sheet of your excel
To call set and parameters from the excel

## Slide 101: Advanced Functionality: Data Exchange with Microsoft Excel
Using the first case, Solar PV Integration, we can transform the model into using excel as an interface by modifying the declaration of input and output data.
Previous codes
Added codes
Put the name of your excel output data.
Put the name of the first sheet of your excel

## Slide 102: Advanced Functionality: Data Exchange with Microsoft Excel
Excel Input
Calling the data from the pre-defined position in the same excel
Horizontal Dimension,
1 reflect only 1 row of horizontal dimension related to data categorized using set
No Dimension, meaning the data is called as it is at its predefined position
Users need to define the position of data in the first sheet of excel (name of sheet is user-defined). The first column reflects the data type, whether set or par (parameter). The second column reflects the name of the input data declared in GAMS. The third column reflects the position of data in Excel.
Vertical Dimension

## Slide 103: Advanced Functionality: Data Exchange with Microsoft Excel
Excel Output
Reflect the position of output data in the same excel
Users need to define the position of data in the first sheet of excel (name of sheet is user-defined). The first column reflects the data type, whether set or par (parameter) or var (variable). The second column reflects the name of the input data declared in GAMS. The third column reflects the position of data in Excel.
Vertical Dimension
Horizontal Dimension,
1 reflect only 1 row of horizontal dimension related to data categorized using set
No Dimension, meaning the data is called as it is at its predefined position

## Slide 104: Further Readings
GAMS’s User’s Guide at https://www.gams.com/latest/docs/UG_MAIN.html
GAMS World Forum at https://forum.gamsworld.org/
GAMS’s case studies https://www.gams.com/stories/
GAMS MIRO https://www.gams.com/sales/miro_facts/
GAMS Engine https://www.gams.com/engine/installation.html
To view a library of previous models coded in GAMS from other authors, open GAMS Studio>GAMS>Model Library Explorer